## Slide 1: Viscosity Ratio Identification in the Buckley-Leverett Model Using PINN
Authors: Samson Dawit Bekele, Timur Imankulov, Yerzhan Kenzhebek
Department of Computer Science, Al-Farabi Kazakh National University
Presenter: Samson Dawit Bekele
samsondawitb@gmail.com

## Slide 2
Motivation and Applications
Congress of the Kazakhstan Mathematical Society 2026
Why Parameter Identification Matters
The Challenge
Fluid parameters like govern saturation front propagation but cannot be measured directly in underground reservoirs.
Traditional Approach
History matching: iterative PDE-solver inversion. Expensive (100s of runs), mesh-dependent, struggles near discontinuities.
Our Approach: Inverse PINN
Learn and simultaneously from sparse, noisy observations. One training run, no mesh, physics constraints built in.
Application Areas
Enhanced Oil Recovery
Water-flooding and polymer flooding. controls sweep efficiency and breakthrough time. Inaccurate leads to poor production forecasts.
Geological Storage
Supercritical CO2 displaces brine in aquifers. Leakage risk depends on mobility ratio. BL is a standard screening model.
Geothermal Systems
Steam-water two-phase flow. Temperature-dependent viscosities make estimation essential for heat extraction.
Hydrogen Underground Storage
Emerging application. H2/brine mobility ratios are uncertain. PINN-based inversion enables rapid real-time calibration.

## Slide 3
The Buckley-Leverett Forward Model
Hyperbolic conservation law for two-phase incompressible flow
Governing PDE (with viscous regularization):
(vanishing viscosity, annealed to 0) - water saturation field
Initial and Boundary Conditions:
- dry reservoir - water injection (left) - production (right)

## Slide 4
Shock Dynamics - Analytical BL Profiles
$M$ shifts the shock front position and changes displacement efficiency
Congress of the Kazakhstan Mathematical Society 2026

## Slide 5
The Inverse Problem
Recover from sparse, noisy saturation measurements
Congress of the Kazakhstan Mathematical Society 2026
Given: observations
Find: (viscosity ratio) and (saturation field) simultaneously
Ill-posedness
The map observations is many-to-one for small . Physics constraints regularize the problem.
Moving discontinuity
The shock position depends nonlinearly on . Small changes in can shift the front significantly.
Noise sensitivity
Observations near the shock front are most informative but also most affected by measurement noise.
Computational cost
Traditional adjoint methods need PDE solves. PINN amortizes this cost into one training run.

## Slide 6
Inverse PINN Architecture
workflow diagram of the full inverse learning pipeline
Congress of the Kazakhstan Mathematical Society 2026

## Slide 7
Model Architecture, Loss Function, and Training
Congress of the Kazakhstan Mathematical Society 2026
Neural Network
Input: - 2D (position and time) Input: is NOT an input - it is a learnable parameter Hidden: 30 layers x 50 neurons = 1,500 hidden units Activation: tanh (smooth, suitable for PDE problems) Output: 1 neuron + sigmoid Params: 74,151 total (Xavier initialization) Learnable scalar (torch.nn.Parameter): Init: True:
Optimized jointly with via backprop Vanishing viscosity stabilization: PDE modified: - prevents shock divergence Corresponds to cells of smoothing in 300-pt grid
Loss Function and Training
Composite loss (all weights = 1.0): - PDE residual at 50,000 LHS points
- initial condition at 512 points - boundary conditions - sensor mismatch at points (primary driver of M)
Optimizer: Phase 1: Adam - 2,000 epochs LR halved at epochs 700 and 1,350 Phase 2: L-BFGS - 1,000 steps, lr = 1.0 (2nd-order polish)

## Slide 8
Training Dynamics - Loss Convergence
Adam phase: 2,000 epochs | N=50 sensors, 5% noise,
Congress of the Kazakhstan Mathematical Society 2026

## Slide 9
Experimental Design
Systematic ablation: two independent research questions
Congress of the Kazakhstan Mathematical Society 2026
RQ1 - Data Efficiency
Question: How many sensor observations are needed to accurately identify ? Varied: Fixed: Noise
Architecture: 30 layers x 50 neurons Collocation: 50,000 LHS points Training: Adam(2000) + L-BFGS(1000)
RQ2 - Noise Robustness
Question: How much measurement noise can the inverse PINN tolerate? Varied: Fixed:
Architecture: 30 layers x 50 neurons Collocation: 50,000 LHS points Training: Adam(2000) + L-BFGS(1000)

## Slide 10
Data Generation - Latin Hypercube Sampling
Congress of the Kazakhstan Mathematical Society 2026
Why LHS over uniform random?
Full coverage
Guarantees each row and column of the domain is sampled exactly once.
No clustering
Avoids accidental gaps where the PDE residual is never enforced.
Noise injection
sensor points have Gaussian noise added to true values.
Scale
50,000 collocation + 512 IC + sensor pts per experiment.

## Slide 11
What Sensor Data Looks Like at Different Noise Levels
50% noise fundamentally changes what the optimizer sees
Congress of the Kazakhstan Mathematical Society 2026

## Slide 12
RQ1 Results - Data Efficiency
Parameter error, convergence, and L2 accuracy across
Congress of the Kazakhstan Mathematical Society 2026

## Slide 13
RQ1 - Diminishing Returns Analysis
The first 50 sensors provide most of the gain
Congress of the Kazakhstan Mathematical Society 2026
Key insight: the 10 to 50 sensor transition yields the steepest error drop. N=100 gives only marginal improvement over N=50. N>100 shows no monotone improvement, suggesting optimization variance dominates data quantity.

## Slide 14
RQ1 - Saturation Profiles: N=10 vs N=500
Time snapshots at | 5% noise
Congress of the Kazakhstan Mathematical Society 2026

## Slide 15
RQ1 - Best Case: N=500 Saturation Profile
PINN captures the shock front accurately across the full time domain
Congress of the Kazakhstan Mathematical Society 2026
| |

## Slide 16
RQ2 Results - Noise Robustness
Robust 0-20% noise | catastrophic failure at 50%
Congress of the Kazakhstan Mathematical Society 2026

## Slide 17
RQ2 - Saturation Profiles: 5% vs 50% Noise
Same N=50 sensors - noise level determines whether is recoverable
Congress of the Kazakhstan Mathematical Society 2026
| |

## Slide 18
Why Does the Method Fail at 50% Noise?
Structural analysis of the optimization landscape
Congress of the Kazakhstan Mathematical Society 2026
Signal overwhelmed
At , noise std = 0.5 (saturation range is 0-1). Sensor 'observations' are essentially random numbers. The data loss points in wrong directions.
False minimum in $M$
is found because it fits the noisy observations better than does - noise creates a spurious loss valley. L2 saturation error jumps from 0.07 to 0.325.
Physics loss cannot compensate
is satisfied (shock structure is learned) but for the wrong . The physics constraint alone cannot uniquely determine when observations carry no signal.
Mitigation strategies
- Increase (more observations reduce noise impact) - Ensemble averaging over multiple noise realizations - Bayesian PINN with uncertainty quantification - Strong prior on range if domain knowledge exists

## Slide 19
L2 Error Breakdown by Time Step
Heatmap: rows = experiment, columns = time snapshots
Congress of the Kazakhstan Mathematical Society 2026
Observation: early times () are consistently harder - the shock is steeper. Late times () show lower absolute error across all experiments.

## Slide 20
Complete Experiment Results
Color-coded by parameter error severity: green < 25%, yellow 25-31%, red > 30%
Congress of the Kazakhstan Mathematical Society 2026

## Slide 21
Key Insights and Discussion
Congress of the Kazakhstan Mathematical Society 2026
1 Simultaneous recovery works
The PINN successfully learns both and scalar in a single training run. No separate calibration step needed.
2 Saturation accuracy exceeds parameter accuracy
Even when , the saturation field L2 error is below 0.05-0.07. The network compensates with a good field even for a slightly wrong .
3 Data efficiency threshold around N=50
Approximately 50 sensor observations achieve parameter error. Doubling to 100 gives less than 1% additional improvement. Rule of thumb: one sensor per of the spatial domain.
4 Robustness limit: 20% noise
Stable recovery across 0-20% noise. The 50% failure is an extreme case (SNR < 1). Noise regularization or smoothing sensor data would extend this range.
5 Vanishing viscosity is non-negotiable
Without , PDE loss diverges near the shock and training fails. corresponds to grid cells of smoothing.
6 L-BFGS matters for M convergence
Adam finds a good basin; L-BFGS provides the final convergence. Without L-BFGS, typically has 5-8% more error.

## Slide 22
Future Directions
Congress of the Kazakhstan Mathematical Society 2026
Vanishing viscosity annealing
Gradually reduce during training (curriculum strategy). Recover the true inviscid BL solution in the limit. Preliminary results suggest 5-8% further accuracy gain.
Bayesian inverse PINN
Treat as a random variable with prior . Posterior over quantifies uncertainty from sparse data. Critical for risk-aware subsurface decisions.
Multi-parameter identification
Extend to simultaneously identify , relative permeability exponents, and injection rate from production history data. More realistic history matching scenario.
Real field data validation
Apply to synthetic well-log saturation data with realistic spatial heterogeneity (layered permeability). Test transfer learning from synthetic pre-training.
2D / multi-dimensional extension
Buckley-Leverett in 2D with gravity: richer shock structures. Requires domain decomposition PINN (cPINN / XPINN) for scalability.
Ensemble and active learning
Train ensemble of PINNs to quantify epistemic uncertainty. Use active learning to select maximally informative sensor locations. Optimal sensor placement could halve required .

## Slide 23: Thank you for your attention! Questions?

## Slide 24
References
Congress of the Kazakhstan Mathematical Society 2026
[1] Buckley and Leverett (1942)
Mechanism of fluid displacement in sands. Transactions of the AIME, 146, 107-116.
[2] Raissi, Perdikaris and Karniadakis (2019)
Physics-informed neural networks: A deep learning framework for solving forward and inverse problems involving nonlinear PDEs. J. Comput. Phys., 378, 686-707.
[3] Jagtap, Kharazmi and Karniadakis (2020)
Conservative physics-informed neural networks on discrete domains for conservation laws: Applications to forward and inverse problems. CMAME, 365, 113028.
[4] Coutinho et al. (2023)
Physics-informed neural networks with adaptive localized artificial viscosity. J. Comput. Phys., 489, 112265.